## Slide 1
A Task-Oriented Executable Modeling
Framework for Smart Chemical Laboratories
Beijing Information Science and Technology University
Presenter: Tao Yu | Corresponding author: Chun Zhao
EUROSIM 2026 · Genova, Italy
Notes: Good morning, everyone. My name is Tao Yu, from Beijing Information Science and Technology University. Today I will present our work, A Task-Oriented Executable Modeling Framework for Smart Chemical Laboratories.
We focus on how a laboratory task moves from an intention to device execution. Our aim is to describe devices, task logic, and operating rules through models, and to make their execution semantics explicit. This becomes especially relevant when large language models participate in laboratory decision-making and control.

## Slide 2
1 Outline
• Background and problem
• Unified modeling framework
• Execution mechanism
• Implementation and case study
• Simulation extension
• Conclusions
From modeling requirements to a shared device execution path.
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
1/10
Notes: I will begin with the background and the execution-boundary problem. I will then introduce the overall modeling framework and explain its resource, workflow, and constraint layers.
Next, I will show how these models cooperate along a shared device execution path. A reactor-heating case in SmartLab 2.0 illustrates the mechanism. Finally, I will discuss a simulation feedback loop as an extension and summarize the main contribution.

## Slide 3
2 Background: execution boundaries with LLMs
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
2/10
Laboratory automation is expanding from predefined workflows
to decision-making and control involving large language models (LLMs).
Every task requires four aspects to be made explicit:
Resources
How they are organized and used
States
How they evolve during execution
Data
How they are generated and passed
Boundaries
Whether execution remains allowed
With LLMs, execution boundaries become more pressing:
What may an LLM request, and under what conditions may it execute?
Principle: no privileged bypass. All device requests follow the same execution path.
An executable framework must unify resources, state evolution, data flow, and boundary checks.
LLM participation makes shared execution boundaries essential.
Notes: Laboratory automation is expanding from predefined workflows toward decision-making and control involving large language models, or LLMs.
Regardless of whether an intention comes from a person, a workflow, or an LLM, every task requires four aspects to be made explicit. How are resources organized and used? How do device states evolve? How are data generated and passed between steps? And does execution remain within the allowed boundaries?
LLMs make the boundary question more pressing. What requests may an LLM make, and under what conditions may those requests execute? Our principle is that an LLM must not have a privileged path directly to a device. Its requests must enter the same execution mechanism as other requests.
This motivates an executable framework that brings resource organization, state evolution, data flow, and boundary checks together. The next question is how to organize these modeling responsibilities.

## Slide 4
3 Unified modeling framework
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
3/10
Model the execution objects as resources, the task process as a workflow, and operating rules as constraints.
Cross-layer protocol Π: control signals, data types, port relations, and execution feedback
Workflow layer
Previous node
Execution node
Next node
Workflow node
Variable space
Task variables / Attribute links
Node lifecycle
Execution phase and outcome
Control interfaces / Data ports
Signals / Input and output data
Trigger: condition → action
Update state / Emit signals
Resource layer
Device object model
Capability model
Attributes and capabilities
Operation parameters
Interfaces / Adapter contract
Intrinsic constraints
State machine
Request and state checks
Transitions and commands
Feedback-driven updates
Capability binding
Requests / Control signals
State / Data feedback
Constraint layer
Observation space
Device state, attributes / Task context
Constraint rules
Laboratory baseline / Task rules
Handling actions
Device actions / Warn / Alarm / Abort
Node variables
Task context
Device state / Measurements
Actions return through node / state-machine interfaces
Resources define capability and state; workflows organize tasks and data; constraints define boundaries.
Notes: We organize the framework by examining what a laboratory task needs to express. The objects used to perform the task become resource models. The order of operations, data dependencies, and progression conditions become a workflow model. The rules that define allowed execution become constraint models.
The diagram therefore has three modeling layers. The workflow layer is on the left, the resource layer is on the right, and the constraint layer observes both from below. The cross-layer protocol, Pi, defines their control signals, data types, port relations, and execution feedback.
The four execution concerns do not map mechanically to four separate layers. Resources represent device capabilities and states. Workflows organize steps, node lifecycles, and data relationships. Constraints define execution boundaries. State and data are shared concerns across these layers.
Notice the distinction between capability binding and runtime interaction. A node is bound to a device capability. During execution, it sends a request and receives state and data feedback. Constraints observe the relevant model values and return handling actions through model interfaces.
This gives the system both an explicit modeling structure and a common basis for execution. Let us first look at the resource layer.

## Slide 5
4 Resources: capabilities and state machines
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
4/10
A device object combines its capability model with a state machine to describe what it can do and how it executes.
Capability model
Defines attributes, capabilities,
and operation requirements.
State machine
Handles requests in the current state,
issues commands, and processes feedback.
Shared entry point
People, workflows, and LLMs
follow the same state rules.
Resource layer
Device object model
Capability model
Attributes and capabilities
Operation parameters
Interfaces / Adapter contract
Intrinsic constraints
State machine
Request and state checks
Transitions and commands
Feedback-driven updates
Capability definitions and state evolution jointly describe device operation semantics.
Notes: The resource layer represents each device as a device object model. The stacked outlines indicate multiple device objects, while the front object shows the common internal structure: a capability model and a state machine.
The capability model describes what the device can do. It defines attributes, available operations, parameters, interfaces, the Adapter mapping contract, and intrinsic constraints. For a reactor, heating is a capability, temperature is an attribute, and a heating request includes a target temperature. The contract links a model-level operation to the Adapter interface.
The state machine describes how a request is executed. It checks the request against the current state and the capability definition, applies the relevant transition actions, and issues commands through its output interface. Returned events and measurements update the device model.
People, workflows, and LLMs all enter through this device model and follow the same rules. We now need to organize individual operations into a complete task.

## Slide 6
5 Workflows: nodes, interfaces, and triggers
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
5/10
Workflows organize steps and data dependencies; nodes coordinate through interfaces and triggers.
Workflow layer
Previous node
Execution node
Next node
Workflow node
Variable space
Task variables / Attribute links
Node lifecycle
Execution phase and outcome
Control interfaces / Data ports
Signals / Input and output data
Trigger: condition → action
Update state / Emit signals
Feedback updates variables; trigger conditions determine requests and progression to the next step.
Notes: The workflow layer organizes task steps and their data dependencies. At the top, a previous node, an execution node, and a next node are connected through their progression relationships. The execution node can bind to a device capability and request an operation.
The lower part expands that node. Its variable space holds task values and links to relevant device attributes. Its lifecycle represents the execution phase and outcome. Control interfaces carry signals, while data ports describe inputs and outputs.
The trigger connects these parts. It reads variables, interface signals, and lifecycle information. When a condition holds, it performs the defined action, such as updating a variable or state, issuing a request, or activating a subsequent node.
For example, a heating node receives an activation signal and requests heating when its preconditions hold. Temperature feedback updates the node's variables. The trigger then evaluates the completion condition. Receiving feedback alone does not mean the task is complete.
These elements form one semantic unit. The task logic is expressed in the model, and the execution mechanism follows that logic.

## Slide 7
6 Constraints: observation and handling actions
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
6/10
Observe resource state and task context together, then return actions through the appropriate interfaces.
Workflow layer
Node lifecycle and task variables
Execution context
Resource layer
Device state and attributes
Measurements
Constraint layer
Observation space
Device state, attributes / Task context
Constraint rules
Laboratory baseline / Task rules
Handling actions
Device actions / Warn / Alarm / Abort
Workflow observations
Resource observations
Actions → Node / State-machine interfaces
Intrinsic constraints
Handled by the device state machine
Laboratory baseline constraints
Continuously supervise the laboratory
Task constraints
Active during the associated task
Notes: The constraint layer observes execution and responds when a rule is triggered. The workflow provides node lifecycle information, task variables, and execution context. The resource layer provides device state, attributes, and measurements.
These values form the observation space. Constraint rules evaluate the observed values in context and produce handling actions. Depending on the rule, an action may operate on a device, issue a warning or alarm, or abort a task. Actions return through node or state-machine interfaces. Device actions therefore continue through the normal Adapter path.
We distinguish three kinds of constraints. Intrinsic constraints belong to the device capability and state rules and are handled locally by the device state machine. Laboratory baseline constraints continuously supervise laboratory operation. Task constraints apply during the associated task.
The constraint layer is not a serial forwarding stage through which every command must pass. It observes execution across layers and returns actions when required. Having defined the objects, task process, and rules, we can now connect them through the execution path.

## Slide 8
7 Shared device execution path
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
7/10
Workflows organize steps; state machines and Adapters execute device requests and return feedback.
Workflow layer
Exec. node
Exec. node
Exec. node
Device model layer
Device model
Device model
Device model
Adapter layer
Adapter
Adapter
Adapter
Physical device
Physical device
Physical device
Physical device
Run
signal
State
feedback
Control
command
Data
feedback
Device
command
Data
status
Workflow node
Control interfaces / Data ports
Variable space
Node lifecycle
Trigger: condition → action
Read variables, interface signals, and lifecycle
Update variables and state; emit signals
Control request / Parameters
Execution state / Data
Device state machine
Capability model → state machine: operation + Adapter contract
Request handling
Check request and state
State transition
Apply transition actions
Command output
Generate command from contract
Events and telemetry → Update device state and attributes
Standard command
Device events / Measurements
Adapter
Command mapping
Upper-layer command → Device protocol
Feedback conversion
Device data → Events / Telemetry
Device command
Measurements / Status
Physical device: perform operations and return measurements and status
People, workflows, and LLMs share the device-model entry point, state rules, and constraints.
Notes: This diagram shows how the models cooperate during a device operation. On the left, the workflow organizes steps horizontally. An individual operation proceeds through the device model, the Adapter, and the physical device. Requests and commands move downward; state and data feedback move upward.
On the right, the workflow trigger issues a request with operation parameters. The capability model supplies the operation definition and the Adapter mapping contract to the device state machine. The state machine checks the request against the current state, applies the transition actions, and generates the agreed upper-layer command according to that contract. The Adapter then maps the command sent by the upper layer into the device protocol or device instruction.
Feedback returns through the corresponding interfaces. The Adapter converts device data into events and telemetry. The device model updates its state and attributes, and the workflow node receives the relevant execution state and data. Node conditions determine whether execution is complete and whether the next step can begin. Constraints continue to observe and act through the model interfaces.
The workflow route shown here is one example. A person or an LLM may also request a device operation directly, without first using a workflow node. However, the request must still pass through the device model and state machine before reaching the Adapter. This is the shared execution boundary introduced at the beginning.

## Slide 9
8 Implementation and case study: reactor heating
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
8/10
SmartLab 2.0: workflow and state-machine engines execute models; an MQTT Adapter handles communication.
Heating node
Device state machine
Adapter
Reactor
Constraint layer
1 Heat request + parameters
State check and request handling
2 Standard heat command
3 Device heat command
loop
During execution: continuous feedback and constraint observation
4 Temperature / Status
5 Telemetry / State update
6 Execution state / Data
Device state and measurements
Node execution context
alt
[Normal] Completion conditions hold and progression is allowed
Complete node → Emit activation signal → Next step
[Exception example] A stop or abort rule is triggered
Device action: stop / abort request to the state machine
Task action: abort through the node interface
Completion conditions govern progression; temperature violations or device faults trigger constraint handling.
Notes: We illustrate the mechanism with a reactor-heating task in SmartLab 2.0. Workflow and state-machine engines execute the models, and an MQTT Adapter handles device communication. The heating node is bound to the reactor's heating capability and contains its task parameters and completion conditions.
Read the sequence from top to bottom. First, the node sends a heating request with parameters. The state machine checks the request and current state, then sends a standard heating command to the Adapter. The Adapter sends the device command to the reactor.
The loop represents continuous feedback. Temperature and operating status return through the Adapter, update the device model, and become available to the node. Resource state and node context are also observed by the constraint layer.
The lower part separates normal progression from an exception example. When completion conditions hold and progression is allowed, the node completes and activates the next step. If a stop or abort rule is triggered, the constraint mechanism acts through the state-machine and node interfaces. This connects request handling, feedback, completion, and exception handling in one modeled execution process.

## Slide 10
9 Extension: simulation feedback loop
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
9/10
A virtual device instance inside the Adapter runs the simulation; upper-level models and rules stay the same.
LLM
Propose / Revise plan
Workflow / Device request
Analyze feedback
Revise steps, parameters, requests
Feedback refines the plan
Workflow model (optional)
Organize steps and data
Nodes issue device requests
Device model
Capability + State machine
Handle request / Issue command
State checks / Transition actions
Process feedback
Update device state and attributes
Generate workflow
Invoke capability
Direct device request
State / Data feedback
Simulation feedback
State, data, constraint results
Adapter
Execute in the selected mode
Simulation mode
Create once at simulation start
Virtual device instance
One instance for the full run
Respond and evolve state
Return simulated data / status
Hardware mode
Map commands / Convert feedback
Command
State /
Data
Physical device
Execute and return actual data
Device command
Data / Status
Simulation feedback uses the same model updates and constraint checks.
Refine the plan through simulation; the host then initiates hardware execution after acceptance.
Notes: This extension uses simulation feedback to refine an experimental plan while preserving the same device execution path.
On the left, an LLM may generate a workflow model or issue a direct device request. Both routes enter the device model and reach the Adapter through its state machine. The workflow is optional; the device model is the common entry point.
At the start of a simulation, the Adapter creates a virtual device instance corresponding to the physical device instance. The same virtual instance is used throughout that simulation run. It responds to commands, evolves its state, and returns simulated measurements and operating status.
The upper layers process this feedback as device data. The device model updates normally. If a workflow is involved, its nodes evaluate triggers and advance normally. Constraint rules also continue to observe the resource state and task context.
The resulting state, data, and constraint outcomes return to the LLM. It can revise the steps, parameters, or device requests and simulate the revised plan again. This is the feedback loop used to improve the experimental plan.
After the host system accepts the simulation result, it initiates hardware execution and selects the Adapter's hardware mode. The Adapter does not decide whether the simulation has passed, and it does not switch to hardware execution on its own. Only hardware mode is connected to the physical device. The upper-level models, interfaces, and execution rules remain the same.

## Slide 11
10 Conclusions
Thank you. Questions are welcome.
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
10/10
Unified modeling
Resources, workflows, and constraints describe laboratory task execution.
Explicit semantics
Variable spaces, interfaces, triggers, and state machines define execution.
Shared execution
People, workflows, and LLMs use the same path, with a simulation extension.
Models describe the laboratory and its tasks; shared semantics drive execution.
Notes: To conclude, the framework provides a unified way to model laboratory task execution. Resources describe device capabilities and states, workflows describe task steps and data relationships, and constraints describe operating boundaries.
The system also makes execution semantics explicit through variable spaces, interfaces, triggers, lifecycles, and state machines. Specific laboratory resources and task logic are expressed in models, while a common mechanism executes those models. This gives the framework a clear structure and makes the execution process explainable at the model level.
Finally, people, workflows, and LLMs share the same device execution path. The simulation extension uses this path to obtain feedback and revise a plan before hardware execution. This brings us back to the original question: an LLM may propose what to do, while the shared model and constraint mechanisms govern how the request executes.
Thank you for your attention. I welcome your questions.