## Slide 1
A Task-Oriented Executable Modeling
Framework for Smart Chemical Laboratories
Beijing Information Science and Technology University
Presenter: Tao Yu Corresponding author: Chun Zhao
EUROSIM 2026, Genoa, Italy
Notes: Hello, everyone. My name is Tao Yu, from Beijing Information Science and Technology University. Today I will present our work, A Task-Oriented Executable Modeling Framework for Smart Chemical Laboratories.
We focus on how a laboratory task moves from an intention to device execution. Our aim is to describe devices, task logic, and operating rules through models, and to make their execution semantics explicit. This becomes especially relevant when large language models participate in laboratory decision-making and control.

## Slide 2
1 Outline
• Background and motivation
• Unified modeling framework
• Shared execution path
• Implementation and case study
• Simulation feedback loop
• Conclusions
How models define and control laboratory task execution.
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
1/10
Notes: I will begin with the background and the execution-boundary problem. I will then introduce the overall modeling framework and explain its resource, workflow, and constraint layers.
Next, I will show how these models cooperate along a shared device execution path. A reactor-heating case in SmartLab 2.0 illustrates the mechanism. Finally, I will discuss a simulation feedback loop as an extension and summarize the main contribution.

## Slide 3
2 Background: limits on LLM device control
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
2/10
Laboratories already automate task workflows.
Large language models (LLMs) now also contribute to planning and device control.
Every task must specify:
Resources
Resource organization and use
States
State changes during execution
Data
Data generation and transfer
Boundaries
Conditions for allowed execution
LLM device control requires explicit limits:
Which operations may an LLM request, and when are they allowed?
All requests enter the device model. LLMs have no direct path to the Adapter.
We therefore model resources, workflows, and constraints in one executable framework.
The framework defines which requests can execute and under what conditions.
Notes: Laboratory automation is expanding from predefined workflows toward decision-making and control involving large language models, or LLMs.
Regardless of whether an intention comes from a person, a workflow, or an LLM, every task requires four aspects to be made explicit. How are resources organized and used? How do device states evolve? How are data generated and passed between steps? And does execution remain within the allowed boundaries?
LLMs make the boundary question more pressing. What requests may an LLM make, and under what conditions may those requests execute? Our principle is that an LLM must not have a privileged path directly to a device. Its requests must enter the same execution mechanism as other requests.
This motivates an executable framework that brings resource organization, state evolution, data flow, and boundary checks together. The next question is how to organize these modeling responsibilities.

## Slide 4
3 Unified modeling framework
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
3/10
Device resources, task workflows, and execution constraints form the three modeling layers.
Protocol Π defines control signals, data types, port connections, and execution feedback
Workflow layer
Previous node
Current node
Next node
Workflow node
Variable space
Variables / Attribute mapping
Node lifecycle
Execution stage and result
Control interfaces / Data ports
Control signals / Data values
Trigger: condition → action
Set values / Send signals
Resource layer
Device object model
Capability model
Attributes and operations
Parameters and interfaces
Adapter mapping contract
Intrinsic constraints
State machine
Check requests and state
Run transition actions
Update state on feedback
Capability binding
Control requests
State and data feedback
Constraint layer
Observation space
Device state / Attributes / Task context
Constraint rules
Laboratory rules / Task rules
Response actions
Device actions / Alerts / Task abort
Node variables
Task context
Device state / Measurements
Actions use node / state machine interfaces
The layers interact through control requests, device feedback, and constraint responses.
Notes: We organize the framework by examining what a laboratory task needs to express. The objects used to perform the task become resource models. The order of operations, data dependencies, and progression conditions become a workflow model. The rules that define allowed execution become constraint models.
The diagram therefore has three modeling layers. The workflow layer is on the left, the resource layer is on the right, and the constraint layer observes both from below. The cross-layer protocol, Pi, defines their control signals, data types, port connections, and execution feedback.
The four execution concerns do not map mechanically to four separate layers. Resources represent device capabilities and states. Workflows organize steps, node lifecycles, and data relationships. Constraints define execution boundaries. State and data are shared concerns across these layers.
Notice the distinction between capability binding and runtime interaction. A node is bound to a device capability. During execution, it sends a request and receives state and data feedback. Constraints observe the relevant model values and return response actions through model interfaces.
This gives the system both an explicit modeling structure and a common basis for execution. Let us first look at the resource layer.

## Slide 5
4 Resources: capabilities and state machines
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
4/10
Each device model combines a capability model with a state machine.
Capability model
Defines operations and the
Adapter mapping contract.
State machine
Checks requests and formats commands
using the capability model's contract.
Shared entry point
All device requests enter
through the device model.
Resource layer
Device object model
Capability model
Attributes and operations
Parameters and interfaces
Adapter mapping contract
Intrinsic constraints
State machine
Check requests and state
Run transition actions
Update state on feedback
The capability model defines available operations. The state machine governs their execution.
Notes: The resource layer represents each device as a device object model. The stacked outlines indicate multiple device objects, while the front object shows the common internal structure: a capability model and a state machine.
The capability model describes what the device can do. It defines attributes, available operations, parameters, interfaces, the Adapter mapping contract, and intrinsic constraints. For a reactor, heating is a capability, temperature is an attribute, and a heating request includes a target temperature. The state machine uses this contract to format a command for the Adapter.
The state machine describes how a request is executed. It checks the request against the current state and the capability definition, applies the relevant transition actions, and issues commands through its output interface. Returned events and measurements update the device model.
People, workflows, and LLMs all enter through this device model and follow the same rules. We now need to organize individual operations into a complete task.

## Slide 6
5 Workflows: nodes, interfaces, and triggers
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
5/10
A workflow defines task steps and data dependencies between nodes.
Workflow layer
Previous node
Current node
Next node
Workflow node
Variable space
Variables / Attribute mapping
Node lifecycle
Execution stage and result
Control interfaces / Data ports
Control signals / Data values
Trigger: condition → action
Set values / Send signals
Node conditions control when to issue requests, complete a step, and activate the next node.
Notes: The workflow layer organizes task steps and their data dependencies. At the top, a preceding node, the current node, and a next node are connected through their progression relationships. The execution node can bind to a device capability and request an operation.
The lower part expands that node. Its variable space holds task values and links to relevant device attributes. Its lifecycle represents the execution phase and outcome. Control interfaces carry signals, while data ports describe inputs and outputs.
The trigger connects these parts. It reads variables, interface signals, and lifecycle information. When a condition holds, it performs the defined action, such as updating a variable or state, issuing a request, or activating a subsequent node.
For example, a heating node receives an activation signal and requests heating when its preconditions hold. Temperature feedback updates the node's variables. The trigger then evaluates the completion condition. Receiving feedback alone does not mean the task is complete.
These elements form one semantic unit. The task logic is expressed in the model, and the execution mechanism follows that logic.

## Slide 7
6 Constraints: monitoring and response actions
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
6/10
Constraint rules monitor device state and task context to determine response actions.
Workflow layer
Node lifecycle and task variables
Execution context
Resource layer
Device state and attributes
Measurements
Constraint layer
Observation space
Device state / Attributes / Task context
Constraint rules
Laboratory rules / Task rules
Response actions
Device actions / Alerts / Task abort
Workflow observations
Resource observations
Actions use node / state machine interfaces
Intrinsic constraints
State machine checks device limits
Laboratory constraints
Apply during laboratory operation
Task constraints
Apply during the specified task
Notes: The constraint layer observes execution and responds when a rule is triggered. The workflow provides node lifecycle information, task variables, and execution context. The resource layer provides device state, attributes, and measurements.
These values form the observation space. Constraint rules evaluate the observed values in context and produce response actions. Depending on the rule, an action may operate on a device, issue a warning or alarm, or abort a task. Actions return through node or state-machine interfaces. Device actions therefore continue through the normal Adapter path.
We distinguish three kinds of constraints. Intrinsic constraints belong to the device capability and state rules and are handled locally by the device state machine. Laboratory constraints continuously supervise laboratory operation. Task constraints apply during the associated task.
The constraint layer is not a serial forwarding stage through which every command must pass. It observes execution across layers and returns actions when required. Having defined the objects, task process, and rules, we can now connect them through the execution path.

## Slide 8
7 Shared device execution path
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
7/10
Device requests pass through the state machine and Adapter. Feedback returns through the model.
Workflow layer
Task node
Task node
Task node
Device model layer
Device model
Device model
Device model
Adapter layer
Adapter
Adapter
Adapter
Physical device
Physical device
Physical device
Physical device
Start
signal
State
feedback
Control
command
Data
feedback
Device
command
Data /
Status
Workflow node
Control interfaces / Data ports
Variable space
Node lifecycle
Trigger: condition → action
Evaluate variables, signals, and lifecycle state
When conditions hold, update values or send signals
Operation request / Parameters
Execution status / Data
Device state machine
Capability model supplies operations and Adapter contract
Request handling
Validate request
State transition
Apply transition actions
Command output
Use Adapter contract
Device feedback updates model state and attributes
Adapter command
Device events / Measurements
Adapter
Command mapping
Adapter command → Device command
Feedback conversion
Device data → Model feedback
Device command
Measurements / Status
Physical device: execute commands and return device feedback
People and LLMs may omit the workflow, but every request must enter the device model.
Notes: This diagram shows how the models cooperate during a device operation. On the left, the workflow organizes steps horizontally. An individual operation proceeds through the device model, the Adapter, and the physical device. Requests and commands move downward. State and data feedback move upward.
On the right, the workflow trigger issues a request with operation parameters. The capability model supplies the operation definition and the Adapter mapping contract to the device state machine. The state machine checks the request against the current state, applies the transition actions, and generates a command for the Adapter according to that contract. The Adapter then translates that command into instructions in the device protocol.
Feedback returns through the corresponding interfaces. The Adapter converts device data into events and telemetry. The device model updates its state and attributes, and the workflow node receives the relevant execution state and data. Node conditions determine whether execution is complete and whether the next step can begin. Constraints continue to observe and act through the model interfaces.
The workflow route shown here is one example. A person or an LLM may also request a device operation directly, without first using a workflow node. However, the request must still pass through the device model and state machine before reaching the Adapter. This is the shared execution boundary introduced at the beginning.

## Slide 9
8 SmartLab 2.0 case study: reactor heating
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
8/10
Workflow and state machine engines run the models. An MQTT Adapter connects to the device.
Heating node
Device state machine
Adapter
Reactor
Constraint layer
1 Heating request
Check state and build command
2 Adapter command
3 Device command
loop
Continuous device feedback and constraint monitoring
4 Temperature / Status
5 State / Measurements
6 Execution status / Data
Device state and measurements
Node execution context
alt
[Normal] Completion conditions hold and constraints permit the next step
Mark node complete and activate the next step
[Exception] A constraint triggers a stop or abort
Request the state machine to stop the operation
Abort the task through the node interface
Temperature feedback alone does not complete the node. Its completion conditions must also hold.
Notes: We illustrate the mechanism with a reactor-heating task in SmartLab 2.0. Workflow and state-machine engines execute the models, and an MQTT Adapter handles device communication. The heating node is bound to the reactor's heating capability and contains its task parameters and completion conditions.
Read the sequence from top to bottom. First, the node sends a heating request with parameters. The state machine checks the request and current state, then sends a heating command in the format defined by the Adapter contract to the Adapter. The Adapter sends the device command to the reactor.
The loop represents continuous feedback. Temperature and operating status return through the Adapter, update the device model, and become available to the node. Resource state and node context are also observed by the constraint layer.
The lower part separates normal progression from an exception example. When completion conditions hold and progression is allowed, the node completes and activates the next step. If a stop or abort rule is triggered, the constraint mechanism acts through the state-machine and node interfaces. This connects request handling, feedback, completion, and exception handling in one modeled execution process.

## Slide 10
9 Extension: simulation feedback loop
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
9/10
The Adapter simulates each device using a virtual instance with the same command and feedback interface.
LLM
Propose a plan
Workflow / Device request
Evaluate feedback
Identify changes to the plan
Revise the plan
Workflow model (optional)
Define steps and data flow
Nodes request operations
Device model
Capability + State machine
Check request / Send command
State rules / Adapter contract
Process feedback
Update device state and attributes
Generate a workflow
Request an operation
Direct device request
State and data feedback
Simulation feedback
Device feedback and constraint results
Adapter
Execution mode set by the host
Simulation mode
Create one instance per device
Virtual device instance
Reuse for the full simulation
Run commands, update state
Return simulated device data
Hardware mode
Translate commands and feedback
Command
State /
Data
Physical device
Execute and return feedback
Device command
Data / Status
Both modes use the same models, interfaces, and constraint checks.
The host starts hardware execution only after accepting the simulation results.
Notes: This extension uses simulation feedback to refine an experimental plan while preserving the same device execution path.
On the left, an LLM may generate a workflow model or issue a direct device request. Both routes enter the device model and reach the Adapter through its state machine. The workflow is optional. The device model is the common entry point.
At the start of a simulation, the Adapter creates a virtual device instance corresponding to the physical device instance. The same virtual instance is used throughout that simulation run. It responds to commands, evolves its state, and returns simulated measurements and operating status.
The upper layers process this feedback as device data. The device model updates normally. If a workflow is involved, its nodes evaluate triggers and advance normally. Constraint rules also continue to observe the resource state and task context.
The resulting state, data, and constraint outcomes return to the LLM. It can revise the steps, parameters, or device requests and simulate the revised plan again. This is the feedback loop used to improve the experimental plan.
After the host system accepts the simulation result, it initiates hardware execution and selects the Adapter's hardware mode. The Adapter does not decide whether the simulation has passed, and it does not switch to hardware execution on its own. Only hardware mode is connected to the physical device. The upper-level models, interfaces, and execution rules remain the same.

## Slide 11
10 Conclusions
Thank you. I welcome your questions.
EUROSIM 2026 · Executable Modeling for Smart Chemical Laboratories
10/10
Unified modeling
Resource, workflow, and constraint models describe task execution.
Explicit semantics
Rules define when actions run and how task and device states change.
Shared execution
Every request uses the device model and Adapter in either execution mode.
Laboratory models supply device and task definitions to a reusable execution mechanism.
Notes: To conclude, the framework provides a unified way to model laboratory task execution. Resources describe device capabilities and states, workflows describe task steps and data relationships, and constraints describe operating boundaries.
The system also makes execution semantics explicit through variable spaces, interfaces, triggers, lifecycles, and state machines. Specific laboratory resources and task logic are expressed in models, while a common mechanism executes those models. This gives the framework a clear structure and makes the execution process explainable at the model level.
Finally, people, workflows, and LLMs share the same device execution path. The simulation extension uses this path to obtain feedback and revise a plan before hardware execution. This brings us back to the original question: an LLM may propose what to do, while the shared model and constraint mechanisms govern how the request executes.
Thank you for your attention. I welcome your questions.